## Slide 1: S6L System Configurator
S6L systems support a maximum of 6 (six) I/O units per AVB network ring.
When the maximum number of I/O units are installed, S6L systems can be configured for a maximum of 192 analog or digital inputs and 112 analog or digital outputs.
Maximum I/O
I/O Sharing
Option Cards
Specs & Measurements
While creating S6L system diagrams, be sure to observe the following guidelines:
A maximum of 2 (two) S6L systems can be connected to each other for I/O Sharing.
In I/O Sharing configurations, ownership (control) of inputs can be shared on a per-I/O-unit basis; ownership (control) of outputs can be shared on a per-output card/slot basis.
For capability and compatibility information on any of the following Option and Expansion Cards, see the VENUE S6L Handbook.pdf:
E6L Engine Option and Expansion Cards Note: Maximum number of cards and installation differ depending on engine type (E6L-192, E6L-144, E6L-112) | AVB-192 Network Card
 | HDX-192 DSP Expansion Card
 | MADI-192 MADI Option Card
 | WSG-HD Waves SoundGrid Option Card
Stage I/O Cards Note: Maximum number of cards/channels varies depending on Stage I/O unit type (Stage 64, Stage 32, Stage 16, Local 16) | SRI Analog Input Card
 | SRO Analog Output Card
 | DSI Digital Input Card
 | DSO Digital Output Card
 | DNT-192 Dante Network Card
For dimension, weight, power, and other specifications, see the S6L Product Specifications.pdf, or the VENUE S6L Handbook.pdf:
Connection Diagrams
When creating diagrams to show specific connections between devices in redundant ring configuration, always follow these guidelines:
All S6L network connections are made from an “A” port to a “B” port (as labelled on each device).
On systems with 2 (two) AVB-192 Network cards in the E6L engine, devices must be connected in two S6L network rings.
All devices support Ethernet (copper) and/or fiber connections. For cable specifications and distance limitations, see the VENUE S6L Installation Guide.pdf.
When creating diagrams for redundant star configurations (v6.3 or later), follow the guidelines in the S6L Luminex Switch Configuration.pdf.

## Slide 2: S6L System Configurator
Download a copy to your local machine.
Save As….and give it a unique name so you can always revert back to the original.
Text in table: Edit the text in the table at the bottom of the slide(s) you’ll be creating (Description, Date, Prepared by, etc.).
Legal and Trademark text is to only be used by Avid personnel.
For your System Configuration Diagram(s):
If all you need is one of the pre-built ones already present, just delete all other slides from your uniquely named deck and skip to step 6 (“Create Deliverable”).
If you need to make custom diagrams, select a pre-built one in the Slides view at far left, right-click on it and choose “Duplicate Slide.” This creates a new slide with the Info table at the bottom, Title fields and whatever graphics are there already. If you instead create a new, blank slide, be sure to copy all those elements from an existing config into your new one.
To assemble your diagram, copy/paste assets from the Assets slides or from any of the pre-built configs.
All the hw images are opaque/non-transparent.
For cables…. PPPT lines and shapes aren’t very easy to work with but you can copy/paste the ones provided and position them to start, or just create new ones and set their color and weight as needed. Be sure to Send to Back for all cables so they’re behind hw images.
To create your deliverable :
Make sure you have entered the appropriate text into the table at the bottom of the slide. Project, Description, Created by, Date, and Page X of Xx (1 of 1, 1 of 2, etc.)
To end up with only the slide(s) you need, you can either delete all the unused/unnecessary slides from your uniquely named PPPT deck and then SaveAs PDF, or SaveAs PDF of the whole thing and delete unused pages from the PDF. I suggest doing it all in PPPT unless you’re certain you have a version of Acrobat (Pro, or DC, or whatever) that lets you Delete Pages (not all versions do).
File Naming – TBD, up to you (whether to name the PDF file by prospective client name, or by system desc., or other).
Recommended - - In Acrobat, check the PDF file to make sure everything looks right, that the links (if any) work, etc.
Recommended – In Acrobat, choose File > Properties and in the Description tab make sure the Title and Author fields are what you want. Then (still in Properties window) go to the Initial View tab and make sure everything there looks OK (defaults are usually fine).
For power, thermal, noise, and other specs, see the separate documents provided (e.g. S6L Product Specifications.pdf).
The Architectural Specifications documents provides text describing everything in a system. Also has minimal power and noise info.
Other documents such as the S6L Handbook.pdf also provide specs, along with additional S6L system configuration examples. You can provide these documents in their entirety, or copy/paste just what you need into a new document.
Create a New Deck
Create Diagrams
Create Deliverable
Specs & Measurements
How to Use This Document
Watermark

## Slide 3: > Single System, Base Configuration: 48 in/8 out
Project - Prepared for - | CREATED BY | PAGE 1 OF 1 | 
DESCRIPTION S6L-24D, E6L-192, 1x Stage 64 Base configuration | DATE | NOT TO SCALE | © 2020 Avid Technology, Inc., (“Avid”), all rights reserved. Avid, the Avid logo, and Avid VENUE are trademarks or registered trademarks of Avid Technology, Inc. or its subsidiaries in the United States and/or other countries. This guide may not be duplicated in whole or in part without the written consent of Avid. Product features, specifications, system requirements, and availability are subject to change without notice.
Stage 64 I/O
48 in/8 out, @ 96k.
Plus 48 MADI splits of all 48 inputs @ 96k or 48k.
Avid VENUE | S6L
E6L-192 Engine
192 Input Processing channels @ 96k.
_ 1x AVB-192 Network Card
Up to 128-channel record/playback via a single AVB Ethernet connection.
Redundant S6L Network Ring
Ethernet (Cat-5e/copper) or fiber-optic
24 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out

## Slide 4: > Single System, Base Configuration: 48 in/8 out
Control Surface back panel Network ports
Project - Prepared for - | CREATED BY | PAGE 1 OF 1 | 
DESCRIPTION S6L-24D, E6L-192, 1x Stage 64 Base configuration | DATE | NOT TO SCALE | 
Stage 64 I/O
48 in/8 out, @ 96k.
Plus 48 MADI splits of all 48 inputs @ 96k or 48k.
Avid VENUE | S6L
Up to 128-channel record/playback via a single AVB Ethernet connection.
24 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out
E6L-192 Engine
192 Input Processing channels @ 96k.
_ 1x AVB-192 Network Card
E6L Engine back panel Network ports
Stage 64 Network ports

## Slide 5: > Single System example 2, Base Configuration 24C-112-Local 16 w/ 48 in/8 out
Project - Prepared for - | CREATED BY | PAGE 1 OF 1 | 
DESCRIPTION S6L-24D, E6L-192, 1x Stage 64 Base configuration | DATE | NOT TO SCALE | © 2020 Avid Technology, Inc., (“Avid”), all rights reserved. Avid, the Avid logo, and Avid VENUE are trademarks or registered trademarks of Avid Technology, Inc. or its subsidiaries in the United States and/or other countries. This guide may not be duplicated in whole or in part without the written consent of Avid. Product features, specifications, system requirements, and availability are subject to change without notice.
Stage 64 I/O
48 in/8 out, @ 96k.
Plus 48 MADI splits of all 48 inputs @ 96k or 48k.
Avid VENUE | S6L
Redundant S6L Network Ring
Ethernet (Cat-5e/copper) or fiber-optic
S6L-16C
16 fader strips
Local 16
8 analog in/8 analog out/
4 stereo AES in/4 stereo AES out
Up to 128-channel record/playback via a single AVB Ethernet connection.
E6L-112 Engine
112 Input Processing channels @ 96k.
_ 2x AVB-192 Network Cards
This one is an example using E6L front view
Placeholder pic

## Slide 6
Project - Prepared for - | CREATED BY | PAGE 1 OF 1 | 
DESCRIPTION S6L-32D, E6L-192, 2x Stage 64 , 4x Stage 16, 3P | DATE | NOT TO SCALE | © 2020 Avid Technology, Inc., (“Avid”), all rights reserved. Avid, the Avid logo, and Avid VENUE are trademarks or registered trademarks of Avid Technology, Inc. or its subsidiaries in the United States and/or other countries. This guide may not be duplicated in whole or in part without the written consent of Avid. Product features, specifications, system requirements, and availability are subject to change without notice.
Avid VENUE | S6L
E6L-192 Engine
192 Input Processing channels @ 96k.
_ 2x AVB-192 Network Cards
_ 3x MADI-192 MADI Option Cards (for converting to Dante devices)
_ 1x WSG-HD Waves SoundGrid Card (for connecting to SoundGrid)
Redundant S6L Network Ring
Ethernet (Cat-5e/copper) or fiber-optic
Stage 64 I/O
64 in/32out, @ 96k.
Plus MADI splits of all 64 inputs @ 96k or 48k.
Stage 64 I/O
64 in/32out, @ 96k.
Plus MADI splits of all 64 inputs @ 96k or 48k.
MADI Splits
To broadcast or backup recording
4x Stage 16 I/O
Each with 16 analog in/
8 analog out, plus 4 out AES/EBU digital
Waves Extreme Server
MADI Out
For converting to Dante
Configuration 3: Single system, max I/O (2x Stage 64 + 4x Stage 16), with 3P connectivity
32 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out
Up to 128-channel record/playback via a single AVB Ethernet connection.

## Slide 7
Stage 64 I/O
64in/32 out, @ 96k.
Plus 64 MADI splits.
Avid VENUE | S6L
Mon
Project - prepared for - | CREATED BY | PAGE 1 OF 1 | 
DESCRIPTION 2x S6L-32D, E6L-192, 2x Stage 64 , 4x Stage 32, 2x Local 16, 3P | DATE | NOT TO SCALE | © 2020 Avid Technology, Inc., (“Avid”), all rights reserved. Avid, the Avid logo, and Avid VENUE are trademarks or registered trademarks of Avid Technology, Inc. or its subsidiaries in the United States and/or other countries. This guide may not be duplicated in whole or in part without the written consent of Avid. Product features, specifications, system requirements, and availability are subject to change without notice.
FOH
Redundant S6L Network Ring
Ethernet (Cat-5e/copper) or fiber-optic
Stage 64 I/O
64in/32 out, @ 96k.
Plus 64 MADI splits.
Up to 128-channel record/playback to/from 1x Pro Tools system. If 2x Pro Tools, max 64-channels each.
4x Stage 32x
Each with 24 in/8out, @ 96k. Plus MADI splits of all 24inputs.
E6L-192 Engine
192 Input Processing channels @ 96k.
_ 2x AVB-192 Network Cards
_ 2x MADI-192 MADI Option Cards (for converting to Dante)
_ 1x MADI-192 MADI Option Card (for Comms)
_ 1x WSG-HD Waves SoundGrid Card (for connecting to SoundGrid)
Waves Extreme Server
MADI Out
For converting up to 128 ch. to Dante
E6L-192 Engine
192 Input Processing channels @ 96k.
_ 2x AVB-192 Network Cards
_ 2x MADI-192 MADI Option Cards (for converting to Dante)
_ 1x MADI-192 MADI Option Card (for Comms)
_ 1x WSG-HD Waves SoundGrid Card (for connecting to SoundGrid)
Waves Extreme Server
MADI Out
For converting up to 128 ch. to Dante
32 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out
32 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out
Up to 128-channel record/playback to/from 1x Pro Tools system. If 2x Pro Tools, max 64-channels each.
MADI Splits
To broadcast or backup recording
Configuration 5: Dual System, max I/O (2x Stage 64 + 4x Stage 32), with 3P connectivity

## Slide 8
Avid VENUE | S6L
Configuration 6: Dual System, max I/O (2x Stage 64 + 4x Stage 32), redundant star configuration using Luminex switches
AVB Switch A
AVB Switch B
When using qualified AVB network switches for a redundant star configuration, refer to the S6L Luminex Switch Guide.pdf for detailed connection and configuration instructions.

## Slide 9: - Assets 1 – S6L Engines and IO -
Stage 64
64x32
Stage 64
48x8
E6L Engine
(front)
E6L Engine w/ 1x AVB
(back)
Stage 64/32
blank
SRO
SRI
DSI
DSO
DNT-192
(Image contains link to DNT-192 on avid.com)
MADI-192
WSG-HD
(Image contains link to MADI-192 page on avid.com)
(Image contains link to WSG-HD page on avid.com)
Note: Stage IO cards are to scale w/ Stage 64 and Stage 32, just copy/paste card(s), rotate (for St32) and place on top of slots. Same for E6L cards (AVB into AVB slot 2, MADI into Option slots 1-4, and WSG into Option slot 6).
AVB-192
Stage 64
-empty-
E6L Engine w/ 2x AVB
(back)
Tip: Some additional E6L configs are already available in some of the Configuration diagrams (e.g. 3x MADI + 1x WSG).
Stage 32x
24 in/8out, @ 96k, plus MADI splits of all 24inputs
Stage 16
16 analog in/ 8 analog out, plus 4 out AES/EBU digital
E6L-112, 1x AVB & 1x WSG (note slot)
Stage 32x
-empty-
Local 16
8 analog in/8 analog out/
4 stereo AES in/4 stereo AES out
front
back

## Slide 10: - Assets 1b – S6L Engines and IO – Network Ports, large
S6L Control Surface Network Ports
Stage 64 Network Ports
Stage 32 Network Ports
Stage 16 Network Ports
Local 16 Network Ports
E6L Engine Network Ports

## Slide 11: - Assets 2 – S6L Control Surfaces -
S6L-32D
32 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out
S6L-24D
24 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out
S6L-48D
48 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out
S6L-24C
24 fader strips, 8 analog in/8 analog out, 8 AES in/8 AES out
S6L-16C
16 fader strips

## Slide 12: - Assets 3 – Pro Tools IO and SYNC
SYNC | HD (back panel)
Pro Tools | HD MADI IO (back panel)
SYNC | HD (front panel)
Pro Tools | HD MADI IO (front panel)
Pro Tools | MTRX (front panel)
Pro Tools | MTRX
(back panel, with Dual MADI exp. card)
Pro Tools | MTRX
(back panel, stock/no exp. cards)
SYNC HD
SYNC | HD (simple)
Pro Tools | HD MADI
Pro Tools | HD MADI (simple)
Pro Tools | MTRX
Pro Tools | MTRX (simple)
Pro Tools | MTRX (front panel)
HD OMNI (back panel)
HD IO (back panel)
HD OMNI (front panel)
HD IO (front panel)
Pro Tools | MTRX Studio (front panel)
Pro Tools | MTRX Studio
(back panel)
Pro Tools | MTRX Studio
(back panel)
HD OMNI
HD OMNI (simple)
HD IO
HD IO (simple)
Pro Tools | MTRX
Pro Tools | MTRX (simple)
Pro Tools | MTRX Studio (front panel)
HD OMNI (front panel)
HD OMNI (back panel)
HD IO (front panel)
HD IO (back panel)
Analog In
Analog Out
Digital IO

## Slide 13: - Assets 3 – PT and Other Avid
(Image contains link to On-Stage page on avid.com)
VENUE On-Stage iPad app
Laptop w/ VENUE logo
Laptop w/ PT logo
PT logo
VENUE logo
S6 M40 24-9-D
S3
Dock
Artist Mix
Mac Pro (“trash can”)
(Image contains link to PT-w-S6L Reqs on K Base)
http://avid.force.com/pkb/articles/Compatibility/What-are-the-system-requirements-for-Pro-Tools-with-S6L
iLok 3rd Gen
iLok 2nd Gen
S1
S4-8_3

## Slide 14: - Assets 4 – Other Non-Avid
Router (wireless)
Router (generic)
1U
2U
3U
4U
5U
Speaker_PA
Sub
Near Fields
2x
Waves ServerOne
Waves Extreme Server
In-Ears
Rack HW
(generic)
Floor Wedges
Line Array - 1
Line Array - 2
Generic small-format mixing desk
Generic large-format mixing desk
Near Field
1x
Waves Extreme Server
Waves ServerOne
Waves ServerOne
(simple)
Waves Extreme Server
(simple)
Laptop _generic
Tablet (generic)

## Slide 15: - Assets 5 – Misc. -
Mic (LDC)
Mic (cond.)
Mic (58-ish)
Bass_electric
Guitar_electric
Mankind’s Greatest
Achievement
Keyboard
AVB Network Switches
Luminex GigaCore 26i
Luminex GigaCore G12
Luminex GigaCore G10

## Slide 16: - Assets 6 – Cables and lines –
These lines are set to Weight = 1 ½. If you resize them they might change weight (thickness).
To set thickness: Double-click on the line/shape you want to change to show the Format bar, then from the Shape Outline menu choose Weight > and choose 1 ½ or whatever works.
Black = S6L AVB (all)
Blue = MADI
Red = Dante
Orange = Waves
Suggested Cable/Line Colors
Dotted = other
To use, copy/paste onto desired slide then “Arrange > Send to Back” to hide behind opaque hw images
MADI
For Comms

## Slide 17: - Assets 7 – Avid Legal, other –
Items on this page are to only be used by Avid personnel, to indicate Avid has created and/or approved the document.
Project - Prepared for - | CREATED BY | PAGE 1 OF 1 | 
DESCRIPTION List control surface(s), engine(s), stage i/o | DATE | NOT TO SCALE | © 2020 Avid Technology, Inc., (“Avid”), all rights reserved. Avid, the Avid logo, and Avid VENUE are trademarks or registered trademarks of Avid Technology, Inc. or its subsidiaries in the United States and/or other countries. This guide may not be duplicated in whole or in part without the written consent of Avid. Product features, specifications, system requirements, and availability are subject to change without notice.